## Slide 1
ESP8266 and using SPIFFS
in-place of SD-Card storage
Program Memory
Serial Peripheral Interface Flash File System
1M Byte Program
3M Byte SPIFFS
Flash Storage

## Slide 2
Program Space
Unused Flash Memory Space
1M-Byte (8M-bit)
3M-Byte (24M-bit)
ESP8266
Used by
SPI
Flash
Filing System
Filing System Implemented in Flash Storage
SPIFFS – the SPI bus Flash memory File System
Unused Flash Memory Space
15M-Byte (120M-bit)
ESP8266
PRO

## Slide 3
SD-CARD
begin
exists
open
remove
rmdir
mkdir
Filing System Comparison SD v SPIFFS
  SPIFFS
  begin
  exists
  open
  remove
  exists
  format
  openDir
  rename
  info
  SPIFFS
  seek
  position
  size
  close
  print
  println
  read
  write
  name
Filing System Objects
File Objects
SD-CARD
seek
position
size
close
print
println
read
write
available
flush
peek
isDirectory
openNextFile
rewindDirectory
See here for SPIFFS Documentation

## Slide 4
Filing System Comparison SD v SPIFFS
// SD Card Write then Read to a file example
#include <SD.h>;
void setup() {
SD.begin(D8);
}
void loop() {
char filename [] = "datalog.txt";
File myDataFile = SD.open(filename, FILE_WRITE);
myDataFile.println("ABCDEFGHIJKLMNOPQRSTUVWXYZ");
myDataFile.println(3.141592654);
myDataFile.close();
myDataFile = SD.open(filename, FILE_READ);
while (myDataFile.available()) {
Serial.write(myDataFile.read());
}
myDataFile.close();
}
// SPIFFS Write then Read to a file example
#include <FS.h>
void setup() {
SPIFFS.begin();
}
void loop() {
char filename [] = "datalog.txt";
File myDataFile = SPIFFS.open(filename, "a");
myDataFile.println("ABCDEFGHIJKLMNOPQRSTUVWXYZ");
myDataFile.println(3.141592654);
myDataFile.close();
myDataFile = SPIFFS.open(filename, "r");
while (myDataFile.available()) {
Serial.write(myDataFile.read());
}
myDataFile.close();
}
Program output/results (File is 34-bytes)
ABCDEFGHIJKLMNOPQRSTUVWXYZ
3.141592654
Program output/results (File is 34-bytes)
ABCDEFGHIJKLMNOPQRSTUVWXYZ
3.141592654

## Slide 5
Filing System Comparison SD v SPIFFS
Implementation Examples/Differences
r Open text file for reading. The stream is positioned at the
beginning of the file.
r+ Open for reading and writing. The stream is positioned at the
beginning of the file.
w Truncate file to zero length or create text file for writing.
The stream is positioned at the beginning of the file.
w+ Open for reading and writing. The file is created if it does
not exist, otherwise it is truncated. The stream is
positioned at the beginning of the file.
a Open for appending (writing at end of file). The file is
created if it does not exist. The stream is positioned at the
end of the file.
a+ Open for reading and appending (writing at end of file). The
file is created if it does not exist. The initial file
position for reading is at the beginning of the file, but
output is always appended to the end of the file.
File myDataFile = SD.open(filename, FILE_WRITE);
File myDataFile = SD.open(filename, FILE_READ);
SD-CARD SPIFFS
File myDataFile = SD.open(filename, filemode);
File myDataFile = SD.open(filename, filemode);

## Slide 6
Filing System Comparison SD v SPIFFS
SPIFFS Things to Note
See here for SPIFFS Documentation
SPIFFS is not a FAT filing system
Filenames are ‘absolute’ and contain the full address
  e.g. “/DATA/filename.dat”
Directories are NOT implemented, however they are simulated
  SD-Card system allows a Directory containing files, SPIFFS does not
  E.g. an SD-Card directory container file called [DATA] can exist and contain a file called ‘filename.dat’
  SPIFFS uses absolute filenames and is implemented as myFile.OPEN(“/DATA/filename.dat”,”r”)
Using Dir dir = SPIFFS.openDir("/DATA"); effectively appends a path filter to files
  Using the example above, File myFile = dir.openFile("r"); then myFile.openFIle(“filename.dat”,”r”); actually opens the file “/DATA/filename.dat”

## Slide 7
Filing System Comparison SD v SPIFFS
SPIFFS Things to Note
See here for SPIFFS Documentation
Filenames path are not case-sensitive and limited to 32 chars. One character is reserved for C string termination (‘\0’), leaving 31 usable characters for filenames (and path)
SPIFFS does not warn you when the 31-character filename limit is exceeded
Flash memory will fail after ~10,000 writes! So keeping writing to a minimum e.g. read many, write few!
    Example: If data logging temp and humidity readings every 10-mins (tt.t,hh.h,dd/mm/yy,hh,mm 25-bytes) then the 3MB flash would be full when 3.1024.1024/25=125829 readings had been recorded. At 10-mins per reading that’s 2.4 years when the data could be overwritten again ~10,000 times, which is more than enough life (2.4x10,000 years) for most applications!
Overall SPIFFS is more versatile than the SD filing system

## Slide 8
GitHub Example Files
See here for GitHub SPI File Repository
Example-1 Writing and Reading from SD-Card file system
Example-2 Writing and Reading from SPIFFS file system
Example-3 Combined SD and SPIFFS Writing and Reading